## Slide 1: Photovoltaic MPPT Charge Controller (PMC2)
Funded by Workforce Central Florida
Mentor: Alan Shaffer - Lakeland Electric
Group 10
Amber Scheurer, EE
Eric Ago, EE
Sebastian Hidalgo, EE
Steven Kobosko, EE

## Slide 2
MPPT Charge Controller
Solar Array
Battery
LCD
Wireless
Wireless
Inverter
System Overview
We intend on designing a charge controller that will implement MPPT and demonstrate it in a fully functional stand-alone photovoltaic system.

## Slide 3: Motivation and Value of Project
Maximize the cost return on investment for solar panels by using Maximum Power Point Tracking (MPPT) algorithms
LCD screen and wireless data transfer
  Useful for testing, research, and maintenance
Potential for industrial scaling
  Incorporate a charge controller system with one controller per panel
Notes: - Save (as much) money on electricity (as possible) - Typical charge controllers just have LED lights Consulting with research engineer at the Florida Solar Energy Center (FSEC)

## Slide 4: Goals
Charge controller has to be inherently low power
Utilize Maximum Power Point Tracking to increase efficiency
User/Researcher Friendly Design
  LCD Screen
  Wireless Data Transfer to Computer Station
  Inexpensive

## Slide 5: Specifications
Solar Panel delivers > 14 V
Total System Power Output > 200 W
12 V Battery with > 30 Ah
Wireless range > 20 m
Approximately 90% Efficient
Charge Controller ~ $200

## Slide 6
The microcontroller interprets the current and voltage from the solar panel to determine maximum power point
IV sensors on the battery determine the charging mode
This information is used to control the DC-DC converter and efficiently charge the battery

## Slide 7
LCD Screen
Boost
Buck
Current Sensor
Voltage Sensor
Charge Controller
PV Panel
Temp. Sensor
Micro Controller
XBee
XBee
MCU
Battery
Inverter
Temp. Sensor
Current Sensor
Voltage Sensor
Light
Sensor

## Slide 8: Solar Panel
Parameter | SunWize SW120
Rated Power | 120 W
Type | Monocrystalline
Peak Power Voltage | 16.7 V
Peak Power Current | 7.18 A
Open Circuit Voltage | 21.0 V
Short Circuit Current | 8.0 A
Dimensions | ~ 2 x 5 ft.

## Slide 9: Microcontroller
ATmega328P
Parameter | Arduino UNO
Chip | ATmega328P
Digital I/O | 14 Pins
Analog Input | 6 Pins
PWM Output | 6 Pins
Communication Protocols | I2C, Serial
2.7 in
Arduino Bootloader
Open Source
2.1 in

## Slide 10
Microcontroller Peripherals

## Slide 11: Current Sensor
ACS711ELCTR-12AB-T
Parameter | ACS711
Sensor Type | Hall Effect
Operating Voltage | 3 – 5.5 V
Current Sensing | -12 – +12 A
Operating Temp. | -40 – 85 °C
4.9 mm
6 mm

## Slide 12: Voltage Sensor
Voltage Divider
Parameter | Voltage Divider
Source | PV panel
Sensor Type | Voltage Divider
Voltage Sense | 0 – 21 V
R1 | 3.2 KΩ
R2 | 1 KΩ
Output Voltage | 0 – 5 V
R1
R2
Vo

## Slide 13: Voltage Sensor
Voltage Divider
R1=2.7kΩ
R2=10kΩ
Vo
Notes: 13

## Slide 14: Irradiance Sensor
TSL235R-LF
Parameter | TSL235R-LF
Operating Voltage | 5 V
Output | Square wave 50% Duty Cycle
Operating Temp. | -25 – 70 °C
Light Wavelength Range | 320 – 1050 nm
Output Frequency | 200 – 300 KHz
4.6 mm
19.46 mm

## Slide 15: Temp Sensor
DS1624
Parameter | DS1624
Operating Voltage | 3 – 5V
Temp. Range | -55 – 125° C
Internal Memory E2 | 256 Bytes
Protocol | I2C
8.5 mm
9 mm

## Slide 16: Wireless Module
24.3 mm
27.6 mm
Parameter | Xbee Series 1
Protocol | 802.15.4
Communication | Serial
Transmitting Power | 1 mW
Outdoor Range | 90 m
Frequency Band | 2.4 GHz
Operating Voltage | 3.3 V

## Slide 17: Wireless Subsystem
Sensor Data

## Slide 18: Battery Comparisons
Deep-Cycle Lead Acid vs. Li-ion
AGM vs. Gel vs. Flooded
Key Parameters
  Cost
  Overcharge Tolerance
  Charge Cycles

## Slide 19: Battery
Sun Xtender PVX-420T
Parameter | Sun Xtender
Chemistry | AGM
Nominal Voltage | 12 V
Capacity | 42 Ah
CCA | 40 A
Number of Charges | 1000
7.71 in
8.05 in
5.18 in

## Slide 20: Battery Charging Stages
Bulk
Absorption
Float

## Slide 21: Inverter
Scobra CPI 1575
Parameter | Scobra/1575
Max Power | 1500 W
Surge | 3000 W
Wave output | Moderate Sine
Input Voltage | 12 V
Output Voltage | 110 – 120 VAC
AC Outlets | 3
USB | 1
83.82 mm
223.5 mm
238.8 mm

## Slide 22: LCD Screen
Parameter | 20 x 4 LCD
Communication | Serial
Color | Black on Green
Operating Voltage | 5 V
Max Current | 60 mA
Notes: 105 x 59.9 mm

## Slide 23
MPPT Algorithms
 | Efficiency | Programming Difficulty | Potential for “error”
Incremental Conductance Method | Highest | Complex | Yes
Perturb and Observe Method | High | Average | Yes
Constant Voltage Method | Low | Low | No

## Slide 24
Voltage
Power
MPP
Pmax
VOC
Perturb and Observe Method
Vmp

## Slide 25
Perturb and Observe Method
Increase
Operating Voltage
Decrease
Operating Voltage
Is current power greater than previous power?
Is current power greater than previous power?
Yes
Yes
No
No
Start/System On

## Slide 26
Adjust PWM
Start
Sensor Read: Battery Voltage
Sensor Read: Battery Current & Voltage
Float or Absorption
I x V > P0
I x V < P0
Increase Voltage
Decrease Voltage
Bulk
Regulated Power Delivered to Battery
LCD: LCD.print Xbee: Serial.write
Notes: Software Diagram & User Interface

## Slide 27
Adjust PWM
Start
Sensor Read: Battery Voltage
Sensor Read: Battery Current & Voltage
Float or Absorption
I x V > P0
I x V < P0
Increase Voltage
Decrease Voltage
Bulk
Regulated Power Delivered to Battery
LCD: LCD.print Xbee: Serial.write
Notes: Software Diagram & User Interface
27

## Slide 28: H-Bridge Topology Buck-Boost DC/DC Regulator
Single Inductor Buck/Boost Architecture
Separate Buck and Boost Operating Modes
Synchronous 4-Switch Operation for Higher Efficiency
Wide Input Voltage Range: 4.5V to 40V
Wide Output Voltage Range: 12V to 15V

## Slide 29: Boost Operation

## Slide 30
Buck Operation

## Slide 31
Distribution of Responsibilities
Eric
Solar
Panel
Power Electronics
Amber
Algorithms
Sebastian
Inverter
Sensors
LCD Screen
User Interface
Steve
Micro- processor
Battery
Wireless
Simulation
PCB Design

## Slide 32: Progress

## Slide 33: Budget
Notes: Cost of Charge Controller vs. Whole System

## Slide 34: Remaining Milestones
Critical Design Review Feb 14
All Parts Ordered Feb 20
Order PCB Feb 29
Meet with Mentor Mar 15
Done Building/Begin Testing Mar 30
Testing Complete Apr 9
Progress Energy Symposium Apr 13

## Slide 35: Remaining Work
Order solar panel, battery, and inverter
Design and order PCB
Complete software
System Integration
Testing

## Slide 36: Anticipated Problems
Designing circuit to handle high power
Heat dissipation
Buck-Boost Circuitry

## Slide 37: Questions?

## Slide 38
Maximum Power Point Tracking
Vin
Vout
Iin
Iout
MPPT
Solar Array
Battery
Sensing PV current and voltage
Sensing battery current and voltage
Adjusting based on MPPT Algorithm

## Slide 39
Example Block Diagram from NXP Semiconductors

## Slide 41
Reference Circuit