## Slide 1
Brandon Frazer
Raymond Lueg
Joe Howard
Ryan Borden
DRONENET: The Quad Chronicles
Raymond Lueg
Notes: Joe

## Slide 2: DRONENET:THE QUAD CHRONICLES Design & System Integration
What system did we design & integrate?
  Four major subsystems that are integrated with one another
  Quadcopter
  Quadcopter Control Terminal (QCT)
  Mobile Landing Platform (MLP)
  MLP Control Terminal (MLPCT)
Raymond Lueg
Notes: Joe

## Slide 3: DRONENET:THE QUAD CHRONICLES Design & System Integration Motivation
Design something fun, potential real-world applications, and challenging
Wireless communication, real-time navigation, (GUI), and power sustainability
Build a flying-air-vehicle
Build a ground vehicle
Utilize 3D printers
Raymond Lueg
Notes: Joe

## Slide 4: DRONENET:THE QUAD CHRONICLES Design & System Integration Goals & Objectives
Quadcopter or Quad
  Autonomous Flight Modes (Landing/Take-off)
  Record telemetry
  Stream live video back to ground
  Stream real-time flight data on-screen over video
  Flight-time of at least 12 minutes
Quad Control Terminal (QCT)
  Plan missions and waypoints and upload OTA
  Control Quadcopter in real-time
  View telemetry from Quad in real-time
Brandon Frazer
Notes: Joe

## Slide 5: DRONENET:THE QUAD CHRONICLES Design & System Integration Goals & Objectives
Mobile Landing Platform (MLP) or Platform
  Extend mission time of Quadcopter
  Successful implementation of a Bedini Motor
  Ability to traverse challenging terrain
  Highly maneuverable and easy to drive
  Locking system for Quadcopter
MLP Control Terminal (MLPCT)
  Multiple control modes
  Touch screen interface
  Joystick-based control
  Secure control of MLP
Brandon Frazer
Notes: Joe

## Slide 6: DRONENET:THE QUAD CHRONICLES Design & System Integration Specifications
Quadcopter
  Flight time up to 15 minutes
  Payload of up to 5 lbs.
  Travel up to 100 meters above sea level
  Travel up to 300 meters radially from the control terminal
Quadcopter Control Terminal
  Map out at least 5 waypoints for a single mission
  Be able to program at least 3 flight modes
Brandon Frazer
Notes: Joe

## Slide 7: DRONENET:THE QUAD CHRONICLES Design & System Integration Specifications
Mobile Landing Platform
  Travel up to 100 meters from the control terminal
  Charge up to 4 batteries using the regenerative
  Ability to navigate through rough terrain
  Ability to lock down the quadcopter while not in flight
  Ability to charge the quadcopter
MLP Control Terminal
  Wirelessly Control the mobile platform
  View all of the real time data streaming from the mobile platform
  Communicate with the Quadcopter control terminal
  Utilize both hardware and software based control systems
  Have a touchscreen LCD display for control and monitoring
  Secure User authentication
Brandon Frazer
Notes: Joe

## Slide 8: THE QUAD CHRONICLES: Quadcopter Design & System Integration
Quadcopter
Joe Howard
Notes: Joe

## Slide 9
APC 1047 Slow Fly Props
10” diameter
4.7” pitch
6500 RPM limit
Estimated Max Thrust: approx. 1.5 – 1.8 lbs. each
THE QUAD CHRONICLES: Quadcopter Propellers
Joe Howard
Notes: Joe

## Slide 10
DJI 2212-920
Stator Size: 22 x 12mm
KV: 920 rpm/V
Max Current: 15A (Given)
Coil Resistance: 0.171 Ω (Calc)
Idle Current: 0.5 Amps (Measured)
Weight: 56g
Multistar 2213-935
Stator Size: 22 x 13mm
KV: 935 rpm/V
Max Current: 15A
Weight: 55g
THE QUAD CHRONICLES: Quadcopter Motors
Joe Howard
Notes: Joe

## Slide 11
ESC 30A OPTO
Max Current: 30A
OPTO-coupled for noise isolation
No calibration required
Compatible Signal Frequency: 30Hz - 450Hz
THE QUAD CHRONICLES: Quadcopter Electronic Speed Controls
Joe Howard
Notes: Joe

## Slide 12
Power Distribution Flow Chart
THE QUAD CHRONICLES: Quadcopter Power Distribution
Joe Howard
Notes: Joe

## Slide 13
Turnigy 5000 mAh 3S
3 Cells
Nom Voltage: 11.1V
Const. Discharge: 200A
Peak Discharge (10sec): 250A
Weight: 443g
Const. Charge Rate: 25A
Internal impedance: .003 Ω
THE QUAD CHRONICLES: Quadcopter Batteries
Turnigy nano-tech 5000 mAh 3S
3 Cells
Nom Voltage: 11.1V
Const. Discharge: 175A
Peak Discharge (10sec): 350A
Weight: 409g
Const. Charge Rate: 40A
Internal impedance: .0012 Ω
Joe Howard
Notes: Joe

## Slide 14
Battery | Voltage | Capacity (mAh) | Const. Discharge Rate | Avg Flight Time | Max Flight Time | Weight | Flight Time to Weight Ratio (sec/g)
Turnigy Nano-Tech 5000 | 11.1 V | 5000 | 175 A | 15:56 | 16:03 | 400g | 2.41
Turnigy 5.0 | 11.1 V | 5000 | 200 A | 12:53 | 14:26 | 451g | 1.92
Turnigy 2650 | 11.1 V | 2650 | 53 A | 8:35 | 8:49 | 244g | 2.17
Battery Testing Data
THE QUAD CHRONICLES: Quadcopter Battery Benchmarks
Joe Howard
Notes: Joe

## Slide 15
DJI Flame Wheel F450
Fiberglass
Weighs 282g
Diagonal Wheelbase of 450mm
VERY STRONG
Built-in PCB for power distribution
THE QUAD CHRONICLES: Quadcopter
Frame
Joe Howard
Notes: Joe

## Slide 16
GoPro HERO3 Camera
Medium Range FPV
Weight < .2 pounds
1080P @ 60 FPS
1280 MHz Transmitter
200 mW 1280 MHz transmitter/receiver with standard antenna
Onscreen Display (OSD) for the camera to stream back to the ground station
Tested at 700ft range with clear picture
Decided against a servo controlled camera system
THE QUAD CHRONICLES: Quadcopter Camera System
Joe Howard
Notes: Joe
*BRANDON

## Slide 17
For a working flight controller we need several components
  Processor, accelerometer, gyroscope, on board programming, GPS, compass, and data logging
Controls motor speed
Allows for autonomous features
THE QUAD CHRONICLES: Quadcopter Flight Controller Requirements
Ryan Borden
Notes: Ryan

## Slide 18
APM 2.6
  Specs work for our application
  Mission Planner software
  Previous experience
  Stability
Controller | Processor | Clock Speed | GPIO | UART | RAM | PWM Channels | Retail Price
APM 2.6 | Atmega 2560 | 16 MHz | 86 | 4 | 8KB | 12 | $240
Pixhawk | Cortex M4 | 168 MHz | 168 | 5 | 256 KB | 14 | $280
THE QUAD CHRONICLES: Quadcopter Flight Controller Selection
Ryan Borden
Notes: Ryan

## Slide 19
THE QUAD CHRONICLES: Quadcopter Flight Controller Details
  Accelerometer and Gryoscope
    MPU-6000
      2.4 Volts
      3.9mA’s
  On-board programming
    ATmega 32U
  Altimeter
    MS5661
      3.6V
      1μA
  Compass
    HMC5883L
      3V
      100μA
Ryan Borden
Notes: Ryan
CHANGE THE DAMN GRID

## Slide 20
Xbee Pro Telemetry
S3B
900 MHz
Up to 215mW transmit power
Up to 9 miles line of sight
Gives us :
  GPS
  Battery monitoring
  Wireless programming
THE QUAD CHRONICLES: Quadcopter
Wireless Telemetry
FPV
1280 MHz
200 mW transmit power
1 mile range
Gives us:
  Live video stream
Ryan Borden
Notes: Brandon or Ray
3DR TELEMTRY PIC

## Slide 21: THE QUAD CHRONICLES: Quadcopter Control Terminal Design & System Integration
Quadcopter Control Terminal
  Plan out waypoints for autonomous missions
  Display and record real-time telemetry data
    Battery life
    GPS
    Altitude
  Calibrate the flight controller
  Customize all parameters for the flight controller
    Limits on speed, fail-safes, and almost anything you could imagine controlling with the Quadcopter
  Verbal warnings are given if there are major issues
Ryan Borden
Notes: Ryan

## Slide 22: THE QUAD CHRONICLES: Quadcopter Control Terminal Mission Planner
Ryan Borden
Notes: Ryan

## Slide 23: THE QUAD CHRONICLES: Quadcopter Control Terminal Mission Planner: Post Flight Data Analysis
Ryan Borden
Notes: Ryan

## Slide 24: THE QUAD CHRONICLES: Quadcopter Control Terminal Mission Planner: Exported GPS Data
Ryan Borden
Notes: Ryan

## Slide 25: THE QUAD CHRONICLES: Quadcopter Control Terminal Mission Planner: Parameter Customization
Ryan Borden
Notes: Ryan

## Slide 26
Mobile Landing Platform
Features
  Mecanum Wheel based drive-train
  Renewable power system
  Quadcopter locking system
  Wireless communications
  Active NeoPixel Lighting
THE QUAD CHRONICLES: Mobile Landing Platform
Platform
Brandon Frazer
Notes: Brandon or Ray

## Slide 27: THE QUAD CHRONICLES: Mobile Landing Platform Electronic Device Architecture
Six total 8-bit microcontrollers
Real-Time Wireless Navigation System with GPS
Ability to communicate with each other and the Platform controller
Wireless Controls for Servos, Mecanum Motors, and Bedini Motor Switching.
Ability to monitor Mecanum Motor Current and Faults, Sonar, and Motion Sensing.
Brandon Frazer

## Slide 28: THE QUAD CHRONICLES: Mobile Landing Platform Electronic Device Architecture Flowchart
Brandon Frazer

## Slide 29
Xbee Pro Controls
900 MHz
63 mW transmit power
1 mile range
$65
Xbee S1 Navigation
2.4GHz
100 mW transmit power
1 mile range
$100
THE QUAD CHRONICLES: Mobile Landing Platform
Wireless Communication
FPV
1263 MHz
100 mW transmit power
1 mile range
$100
Brandon Frazer
Notes: Brandon or Ray
3DR TELEMTRY PIC

## Slide 30
THE QUAD CHRONICLES: Mobile Landing Platform
Platform Master and Slave Controllers
Brandon Frazer
Notes: Brandon or Ray

## Slide 31
THE QUAD CHRONICLES: Mobile Landing Platform
Mecanum Motor Driver Controller
Brandon Frazer

## Slide 32
THE QUAD CHRONICLES: Mobile Landing Platform
Motor Drivers
Brandon Frazer
Notes: Brandon or Ray

## Slide 33
THE QUAD CHRONICLES: Mobile Landing Platform
Platform Peripherals
Ryan Borden
Active NeoPixel lighting
  Based on WS2812 LED drivers
  RGB LEDs
  Controlled using a single data line
    Individually addressed pixels
    Arduino Mini
  5 V, 2-3A
    Low brightness
Programmed two mode
  Runway and Cylon
  Maintenance
Notes: Brandon or Ray

## Slide 34
THE QUAD CHRONICLES: Mobile Landing Platform
Mecanum Wheel Drive-Train
Brandon Frazer

## Slide 35
2-Stage Planetary Gearbox
198 RPM
Stall Current of 22 Amps
Tested Nominal Current ~5 Amps
1210 oz-in (6.3 ft-lb) Torque
THE QUAD CHRONICLES: Mobile Landing Platform
Mecanum Wheel Drive-Train
Brandon Frazer

## Slide 36
THE QUAD CHRONICLES: Mobile Landing Platform
Mobile Platform Power Distribution
Total Current Draw ~30 Amps Nominal
Designed to handle up to 120 Amps Peak (Stall)
Current monitoring of the left and ride side
Current monitoring of the Bedini charging circuit
System voltage and current monitoring
Raymond Lueg
Notes: Brandon or Ray
No more GRID….snow…aka cocaine.

## Slide 37: THE QUAD CHRONICLES: Mobile Landing Platform Power
Solar Panel for supplemental power
Bedini Motor with sensing circuit
  Extends life of battery system
12V battery supply
Raymond Lueg
Notes: Ray

## Slide 38
Regenerative power supply
Referenced design
  Added sensing and switching circuitry
Mounted on mobile platform
THE QUAD CHRONICLES: Mobile Landing Platform
Bedini Motor
Raymond Lueg
Notes: Ray

## Slide 39
THE QUAD CHRONICLES: Mobile Landing Platform
Bedini Motor
Raymond Lueg
Notes: Ray

## Slide 40
THE QUAD CHRONICLES: Mobile Landing Platform
Bedini Motor
Bedini Circuit Diagram
Raymond Lueg
Notes: Ray

## Slide 41
THE QUAD CHRONICLES: Mobile Landing Platform
Bedini Motor
Bedini Schematic
Raymond Lueg
Notes: Ray

## Slide 42
Purpose
  To transport the quad copters safely while on the mobile platform.
Parameters
  Easily controlled by the MLPCT
  Minimal power consumption (Ability to turn off when locked/not in use)
  Stability
Components
  Neodymium magnets
  ¼ Scale Hitech Servos (183 oz-in Torque)
THE QUAD CHRONICLES: Mobile Landing Platform
Quad Locking System
Brandon Frazer
Notes: Brandon or Ray

## Slide 43
THE QUAD CHRONICLES: Mobile Landing Platform
Quad Locking System
Brandon Frazer
Notes: Brandon or Ray

## Slide 44
Mobile Landing Platform Control Terminal
Mobile Platform Brains
Real time monitoring and controls
Touchscreen graphical LCD
Slide potentiometers and push buttons
8-Way Joystick for motor controls
Fingerprint Scanner
THE QUAD CHRONICLES: Platform Carrier Control Terminal Design & System Integration
Brandon Frazer
Notes: Brandon or Ray

## Slide 45: THE QUAD CHRONICLES: Platform Carrier Control Terminal Electronic Device Architecture
Brandon Frazer
Notes: Fix the visio “heading”

## Slide 46
THE QUAD CHRONICLES: Platform Carrier Control Terminal MLPCT Schematic
Brandon Frazer
Notes: Brandon

## Slide 47
THE QUAD CHRONICLES: Platform Carrier Control Terminal MLPCT PCB
Brandon Frazer
Notes: Brandon

## Slide 48
THE QUAD CHRONICLES: Platform Carrier Control Terminal MLPCT Menu System
Brandon Frazer
Notes: Brandon

## Slide 49: THE QUAD CHRONICLES UAV Carrier Control Terminal MLPCT Security System
  Security System
  Secured across Sub-Systems I-IV
  Fingerprint scanner for user authentication
  Certain actions (such as arming the turret or unlocking/landing a Quadcopter) require authentication codes
Brandon Frazer
Notes: Brandon

## Slide 50
200 mW RF Transmitter(TX)-Receiver(RX)
1268MHz operating frequency
GoPro HERO3 mounted on a user-controlled Pan and Tilt Servo System
Mounted with an Ultrasonic Sonar for range
Ability to be viewed through any LCD with RCA inputs
Tested TX range ~700 feet (line of site)
THE QUAD CHRONICLES: Mobile Landing Platform
Camera System
Brandon Frazer

## Slide 51
Quadcopter
  $760
Quadcopter Control Terminal
  $95
Platform
  $2100
Platform Control Terminal
  $280
Misc. Materials
  $350
Brandon Frazer
THE QUAD CHRONICLES: Mobile Landing Platform
Budget

## Slide 52
 | Platform | Regenerative Power System | Platform Control Terminal | Quadcopter | Quadcopter Control Terminal | Administrative
Brandon | X |  | X | X | X | X
Ray | X | X |  |  |  | X
Ryan |  |  |  | X | X | X
Joe |  |  |  | X | X | X
Raymond Lueg
THE QUAD CHRONICLES: Mobile Landing Platform
Division of Labor

## Slide 53
Dr. Richie – Encouragement and Advice
Duke Energy – Funding
Theta Tau Rho Gamma
  Monica Bertram, M.E.
  Sean Delvecchio, M.E.
  Matthew Harrison, M.E.
  Steven Darrow, A.E.
UCF Alumni
  Stephen Sheldon, E.E.
Brandon Frazer
THE QUAD CHRONICLES: Mobile Landing Platform
Acknowledgments

## Slide 54
THE QUAD CHRONICLES: Mobile Landing Platform
Questions
Notes: WEEEEEEEEEEEEEEEEEEEE

## Slide 55: Appendices
Mobile Platform Control Terminal

## Slide 56: Appendices
Platform Master and Slave Controllers

## Slide 57: Appendices
Mecanum Motor Driver Controller

## Slide 58: Appendices
Motor Drivers

## Slide 59: Appendices
Bedini Motor