## Slide 1: Game Qube
UCF Senior Design Group 33
Stephen Monn (CpE)
Omar Alami (CpE)
Matthew Dworkin (CpE)

## Slide 2: Project Description
Game Qube is a video game unit, inspired by the Nintendo Gamecube, that includes games and applications highlighting it’s unique LED cube display.
Game Qube

## Slide 3: Project Specifications
Pixel Resolution: 10 x 10 x 10 = 1000 LEDs
LED Volume Dimension: 10’’x10’’x10’’
Base Dimension: 12’’x12’’x4’’
Visible Sides of Cube: Top, All Sides (not Bottom)
LED Color: Multiple colors supported
Color Depth: 8bit = 256 colors per LED
LED Refresh Rate: at least 60Hz
Input Voltage: 120V AC at 60Hz (Standard Wall Outlet)
Input: Gamecube Controllers
Low Cost

## Slide 4: Modular Design Overview
LED Volumetric Display Control
Central Processing
Volume Based Rendering Software
Handles all graphics and input processing
Handles LED display driving
Data transferred through custom display interface

## Slide 5: Modular Design Overview
LED Volumetric Display Control
Central Processing
Volume Based Rendering Software

## Slide 6: LED Display Goals
Multiplex the LEDs so that they are not all on at once (drive LEDs in smaller chunks)
Low power consumption
Highly responsive interface

## Slide 7: Micro Controller
Model | RAM (kB) | Flash (kB) | Clock (MHz) | Max SPI | I/O Pins
g2553 | 0.5 | 16 | 16 | 2 | 24
g2203 | 0.25 | 2 | 16 | 2 | 24
g2303 | 0.25 | 4 | 16 | 2 | 24
f5529 | 8 | 128 | 25 | 4 | 63
MSP430s

## Slide 8: Memory IC
FIFO Memory
Generally less expensive
Fewer I/O pins
Easy buffer like interface
Asynchronous and simultaneous read and write
CYPRESS CY7C429-25PC
2kx9 memory size
28.5MHz R/W rate
Can be swapped for higher memory capacities

## Slide 9: LED Drivers
Driver | Channels | Transfer Speed | PWM (Brightness) | Dot Correction
STP16CP05 | 16 | 30MHz | No | No
TLC5940 | 16 | 30MHz | Yes | Yes

## Slide 10: LEDs
Specifications
Diffused for better color mixing
Common anode for LED driver compatibility
8mm for low visual obstruction
Layout
Anodes of layers are tied together (10)
Cathodes are common across all layers (300)
10x300 addressable matrix

## Slide 11: LED Control Overview

## Slide 12: Schematic

## Slide 13: Software/Interface
10 Pin Connector
Data
Clock
Sync
LED control software is interrupt based running on a timer
LED cube refreshes at around 300Hz, but is an overkill frequency for rendering frames
Software then only checks for new data after 5 cube refreshes (60Hz)
Cube still refreshes at 300Hz, however, and is then capable of checking after refresh 6, 7, 8, etc.
Gives a supported frame rates of 60Hz, 50.8Hz, 43.6Hz, 38Hz, 33.9Hz
Pins | Function
Data | Pins to write a byte of data
Clock | Clock in the byte of data
Sync | Goes low when all data has been processed. Can be used to keep a constant 60Hz frame rate

## Slide 14: Timing Diagram
Clock
Sync
16.7ms (60Hz)
16.7ms (60Hz)
16.7ms (60Hz)
3.34ms (300Hz)
23.38ms (42.8Hz)

## Slide 15: Testing
LED Stress Testing
All LEDs were individually tested to ensure all colors were appropriately lighting
LEDs were left on for 3hrs. at a constant current of 5mA to ensure reliability over time
Results
Only one bad LED was found out of 1000
All LEDs maintained consistent brightness over long period of time

## Slide 16: Testing
Cube Refresh Rates
Display was tested to ensure a refresh rate of 300 Hz was being achieved
Results
Lights blinked at a noticeable 1 Hz when programmed to blink once every 300 refreshes

## Slide 17: Testing
Interface
Interface was tested to ensure a reliable and consistent data transfer
Results
Successful transfer of byte encoded LED data with little to no display artifacts
Have not yet stressed the interface to determine highest possible refresh rates

## Slide 18: Central Processing
LED Volumetric Display Control
Central Processing
Volume Based Rendering Software

## Slide 19: Central Processing Goals
Supply data to LED cube
Communicate with Gamecube Controller
Control the power
Control any additional features

## Slide 20: Microcontroller Requirements
Enough memory for games and animations: 256kB+
Enough IO pins for 1+ controllers, LED data, and future features: 20+
Easy to program

## Slide 21: Microcontroller Choices
Model | Family | Architecture | Flash (kB) | Clock (MHz) | I/O Pins
Atmel UC3: AT32UC3B0512 | AVR UC3 | 32-bit AVR | 512 | 64 | 60
TI Tiva: TM4C123GH6PM | Cortex-M4 | ARMv7-M (Thumb2) | 256 | 80 | 43
Atmel SAM3S: ATSAM3S8B | Cortex-M3 | ARMv7-M (Thumb2) | 512 | 64 | 64

## Slide 22: Microcontroller Choice
TI Tiva: TM4C123GH6PM
Meets minimum requirements
Easier programming
Launchpad allows for quick testing and as a reference design

## Slide 23: Gamecube Controller
Fits theme
Plenty of buttons
Wired and wireless options
Four pins per controller

## Slide 24: Testing
Gamecube controller timings
Oscilloscope was used to verify that the main microcontroller was able to produce a signal precisely timed so that the Gamecube controller would understand and respond with button data
Results
Successfully sent timed signal and were able to retrieve button data from the controller

## Slide 25: Power
Requirements:
  LED Display: 3.3V, 1A
  TI Tiva: 3.3V
  Gamecube controller: 5V, 3.3V
Options:
  12V Gamecube AC Adapter
  9V AC Adapter
Design:
  12V Gamecube AC Adapter
  DC/DC Converter: 3.3V, 5V

## Slide 26: Board Design

## Slide 27: Software
LED Volumetric Display Control
Central Processing
Volume Based Rendering Software

## Slide 28: Software Goals
Animations
Games
Simple user interface

## Slide 29: Software Block Diagram
Core rendering and program flow
Virtual environment testing interface
Low level microcontroller interface

## Slide 30: Virtual Environment
Virtual representation of our LED Cube
Easy input mapping to keyboard or any convenient PC peripherals
Allows for immediate testing of animations and games
Acts as a quick prototyping environment for testing new ideas before embedded design

## Slide 31: Rendering Engine
Video Driver
Handles rendering primitives to a buffer array
Scene Manager
Keeps track of all items to be rendered in a scene
Scene Nodes
Individual items drawn in a scene
Controller
Handles all things related to input
Runnable
Handles logic loop for anything that can be run from the main menu
1
1
1
*
Main
- Creates a Video Driver, Scene Manager and Controller - Creates all runnables - Handles transitioning between different runnables

## Slide 32: User Interface
Main Menu
(Home)
Snake
Rotator
Other Games
Animations

## Slide 33: Snake
Control a snake’s movement in order to collect dots and make the snake grow longer
Snake can move in x, y, and z directions

## Slide 34: Rotator
Rotate a block so that it can fit through a hole on one side of the cube
The block can rotate left, right, forwards and backwards

## Slide 35: Animation Testing
3D Rendered Wireframes
Display a wireframe mesh of a cube on LED display for possible game applications
Results
Wireframe objects look too distorted on such a low resolution display, especially when not moving

## Slide 36: Administrative Info

## Slide 37: Budget
Item | Price | Qty | Total
10pin Ribbon Cable x1 | $0.99 | 16 | $15.84
Ribbon Cable Sockets x20 | $4.99 | 2 | $9.98
Ribbon Cable Sockets x4 | $1.01 | 1 | $1.01
28pin DIP IC Sockets x5 | $0.99 | 5 | $4.95
TLC5940NT x20 | $17.50 | 1 | $17.50
5mm RGB LEDs x1000 | $60.60 | 1 | $60.60
MSP430F5529 | $0.00 | 1 | $0.00
Resistors/Capacitors | $0.00 | 0 | $0.00
Wire (price/ft) | $0.03 | 500 | $15.00
2kx9 FIFO CY7C429-25PC x5 | $4.99 | 1 | $4.99
Item | Price | Qty | Total
P-Channel MOSFET x20 | $3.19 | 1 | $3.19
LED Matrix Wood Base | $4.99 | 1 | $4.99
LED Matrix Black Paper | $0.33 | 1 | $0.33
LED Matrix Nails | $1.30 | 1 | $1.30
0.1uF Ceramic Capacitors x100 | $0.99 | 1 | $0.99
Broken Gamecube | $0.99 | 1 | $0.99
Sub Total: | $140.67
Shipping: | $31.81
Grand Total: | $172.48

## Slide 38: Work Distribution
 | Omar Alami | Matthew Dworkin | Stephen Monn
Main Controller (Processor/ Power/ Controls) |  |  | 
Main Software (Rendering Engine/ Games) |  |  | 
LED Cube Control (LED Driving/ Display Interface) |  |  | 

## Slide 39: Progress
Main Software (Rendering Engine/ Games)
10% 20% 30% 40% 50% 60% 70% 80% 90% 100%
LED Cube Control (LED Driving/ Display Interface)
Main Controller (Processor/ Power/ Controls)
Stretch Goals
Research
Design
Prototype
Testing
Final Package
Overall: 70%

## Slide 40: Overall Difficulties
Housing Design
Very tricky timings!
IC Coupling
Race conditions
Heap size allocation

## Slide 41: Questions?