## Slide 1: GameQube
UCF Senior Design Group 33
Stephen Monn (CpE)
Omar Alami (CpE)
Matthew Dworkin (CpE)

## Slide 2: Project Description
Game Qube is a video game unit, inspired by the Nintendo Gamecube, that includes games and applications highlighting it’s unique LED cube display.
Game Qube

## Slide 3: Project Specifications
Pixel Resolution: 10 x 10 x 10 = 1000 LEDs
LED Volume Dimension: 10’’x10’’x10’’
Base Dimension: 14’’x14’’x5’’
LED Color: Multiple colors supported
Color Depth: 8bit
Frame Rate: 60Hz
Input Voltage: 120V AC at 60Hz (Standard Wall Outlet)
Input: Gamecube Controllers
Low Cost

## Slide 4: Modular Design Overview
LED Volumetric Display Control
Central Processing
Volume Based Rendering Software
Handles all graphics and input processing
Handles LED display driving
Data transferred through custom display interface

## Slide 5: Modular Design Overview
LED Volumetric Display Control
Central Processing
Volume Based Rendering Software

## Slide 6: LED Display Goals
Multiplex the LEDs so that they are not all on at once (drive LEDs in smaller chunks)
Low power consumption
Highly responsive interface

## Slide 7: LED Control Overview

## Slide 8: Micro Controller
Model | RAM (kB) | Flash (kB) | Clock (MHz) | Max SPI | I/O Pins
g2553 | 0.5 | 16 | 16 | 2 | 24
g2203 | 0.25 | 2 | 16 | 2 | 24
g2303 | 0.25 | 4 | 16 | 2 | 24
f5529 | 8 | 128 | 25 | 4 | 63
MSP430s

## Slide 9: Memory IC
FIFO Memory
Generally less expensive
Fewer I/O pins
Easy buffer like interface
Asynchronous and simultaneous read and write
CYPRESS CY7C429-25PC
2kx9 memory size
28.5MHz R/W rate
Can be swapped for higher memory capacities

## Slide 10: LED Drivers
Driver | Channels | Transfer Speed | PWM (Brightness) | Dot Correction
STP16CP05 | 16 | 30MHz | No | No
TLC5940 | 16 | 30MHz | Yes | Yes

## Slide 11: LEDs
Specifications
Diffused for better color mixing
Common anode for LED driver compatibility
8mm for low visual obstruction

## Slide 12: LEDs
Specifications
Diffused for better color mixing
Common anode for LED driver compatibility
8mm for low visual obstruction
Layout
Anodes of layers are tied together (10)
Cathodes are common across all layers (300)
10x300 addressable matrix

## Slide 13: Schematic

## Slide 14: PCB

## Slide 15: Software/Interface
10 Pin Connector
Data
Clock
Sync
LED control software is interrupt based running on a timer
LED cube refreshes at around 300Hz, but is an overkill frequency for rendering frames
Software then only checks for new data after 5 cube refreshes (60Hz)
Cube still refreshes at 300Hz, however, and is then capable of checking after refresh 6, 7, 8, etc.
Gives a supported frame rates of 60Hz, 50.8Hz, 43.6Hz, 38Hz, 33.9Hz
Pins | Function
Data | Pins to write a byte of data
Clock | Clock in the byte of data
Sync | Goes low when all data has been processed. Can be used to keep a constant 60Hz frame rate

## Slide 16: Timing Diagram
Clock
Sync
16.7ms (60Hz)
16.7ms (60Hz)
16.7ms (60Hz)
3.34ms (300Hz)
23.38ms (42.8Hz)

## Slide 17: Testing
LED Stress Testing
All LEDs were individually tested to ensure all colors were appropriately lighting
LEDs were left on for 3hrs. at a constant current of 5mA to ensure reliability over time
Results
Only one bad LED was found out of 1000
All LEDs maintained consistent brightness over long period of time

## Slide 18: Testing
Cube Refresh Rates
Display was tested to ensure a refresh rate of 300 Hz was being achieved
Results
Lights blinked at a noticeable 1 Hz when programmed to blink once every 300 refreshes

## Slide 19: Testing
Interface
Interface was tested to ensure a reliable and consistent data transfer
Results
Successful transfer of byte encoded LED data with little to no display artifacts
Have not yet stressed the interface to determine highest possible refresh rates

## Slide 20: Central Processing
LED Volumetric Display Control
Central Processing
Volume Based Rendering Software

## Slide 21: Central Processing Goals
Supply data to LED cube
Communicate with Gamecube Controller
Control the power
Control any additional features

## Slide 22: Microcontroller Requirements
Enough memory for games and animations: 256kB+
Enough IO pins for 1+ controllers, LED data, and future features: 20+
Easy to program

## Slide 23: Microcontroller Choices
Model | Family | Architecture | Flash (kB) | Clock | I/O Pins
Atmel UC3: AT32UC3B0512 | AVR UC3 | 32-bit AVR | 512 | 64 | 60
TI Tiva: TM4C123GH6PM | Cortex-M4 | ARMv7-M (Thumb2) | 256 | 80 | 43
Atmel SAM3S: ATSAM3S8B | Cortex-M3 | ARMv7-M (Thumb2) | 512 | 64 | 64

## Slide 24: Microcontroller Choice
TI Tiva: TM4C123GH6PM
Meets minimum requirements
Easier programming
Launchpad allows for quick testing and as a reference design

## Slide 25: Gamecube Controller
Fits theme
Plenty of buttons
Wired and wireless options
Four pins per controller

## Slide 26: Testing
Gamecube controller timings
Oscilloscope was used to verify that the main microcontroller was able to produce a signal precisely timed so that the Gamecube controller would understand and respond with button data
Results
Successfully sent timed signal and were able to retrieve button data from the controller

## Slide 27: Power
Requirements:
  LED Display: 3.3V, 1-2A
  TI Tiva: 3.3V
  Gamecube controller: 5V, 3.3V
Options:
  12V Gamecube AC Adapter
  9V AC Adapter
Design:
  12V Gamecube AC Adapter
  DC/DC Converter: 3.3V, 5V

## Slide 28: Sound Design
Requirements:
  Stereo Input/Output
  Play both music and sound effects simultaneously
  Allow for user to input their own music
Design:
  MSP430g2553
  SD Card for extra ROM
  Op Amp to amplify signal for ADC

## Slide 29: Board Design

## Slide 30: PCB

## Slide 31: Software
LED Volumetric Display Control
Central Processing
Volume Based Rendering Software

## Slide 32: Software Goals
Simple user interface
Games
  Snake
  Pong
  Brick
  Block
Animations
Music Visualizer

## Slide 33: Software Block Diagram
Core rendering and program flow
Virtual environment testing interface
Low level microcontroller interface

## Slide 34: Virtual Environment
Virtual representation of our LED Cube
Programmed using Microsoft Visual C++ 2010 and the Irrlicht Engine
Easy input mapping to keyboard or any convenient PC peripherals
Allows for immediate testing of animations and games
Acts as a quick prototyping environment for testing new ideas before embedded design

## Slide 35: User Interface

## Slide 36: User Interface
Menu
Pause

## Slide 37: Rendering Engine
Video Driver
Handles rendering primitives to a buffer array
Scene Manager
Keeps track of all items to be rendered in a scene
Scene Nodes
Individual items drawn in a scene
Controller
Handles all things related to input
Runnable
Handles logic loop for anything that can be run from the main menu
1
1
1
*
Main
- Creates a Video Driver, Scene Manager and Controller - Creates all runnables - Handles transitioning between different runnables

## Slide 38: Snake
Control a snake’s movement in order to collect dots and make the snake grow longer
Snake can move in x, y, and z directions
Game ends if:
  Snake hits any of the six sides of the cube
  Snake runs into itself

## Slide 39: Pong
Two players move paddles on opposite sides of the cube, bouncing a ball in between
The ball speed will get faster and faster over time
Game ends if:
  A player reaches winning score

## Slide 40: Brick
Based on Atari “Breakout”
One player pong
Player has to destroy all bricks before losing all lives

## Slide 41: Animations
Animations runnable loops through several animations
User can skip any animation using A

## Slide 42: Block
Rotate a block so that it can fit through a hole on one side of the cube
The block can rotate left, right, forwards and backwards
Game ends if:
  Time runs out and block does not fit through hole

## Slide 43: Music Visualizer
Animations controlled by music
View raw waveform of the sound signal
View the presence of frequencies in the sound signal
Input your own music through auxillary

## Slide 44: Administrative Info

## Slide 45: Budget
10pin Ribbon Cable x1 | $0.99 | 16 | $15.84 | $1.00
Ribbon Cable Sockets x20 | $4.99 | 2 | $9.98 | $0.00
Ribbon Cable Sockets x4 | $1.01 | 1 | $1.01 | $0.00
28pin DIP IC Sockets x5 | $0.99 | 5 | $4.95 | $2.51
TLC5940NT x20 | $17.50 | 1 | $17.50 | $2.00
5mm RGB LEDs x1000 | $60.60 | 1 | $60.60 | $22.00
MSP430F5529 | $0.00 | 1 | $0.00 | -
Resistors/Capacitors | $0.00 | 0 | $0.00 | -
Wire (price/ft) | $0.03 | 500 | $15.00 | -
2kx9 FIFO CY7C429-25PC x5 | $4.99 | 1 | $4.99 | $2.00
P-Channel MOSFET x20 | $3.19 | 1 | $3.19 | $0.00
LED Matrix Wood Base | $4.99 | 1 | $4.99 | -
LED Matrix Black Paper | $0.33 | 1 | $0.33 | -
LED Matrix Nails | $1.30 | 1 | $1.30 | -
LED Display PCB | $25.00 | 1 | $25.00 | $0.00
Main Processor PCB | $15.00 | 1 | $15.00 | $0.00
PAM8403 Audio Amplifier | $2.49 | 1 | $2.49 | $0.00
SD Card Pinout | $0.89 | 1 | $0.89 | $0.00
Acrylic | $26.40 | 1 | $26.40 | -
Wood Filler | $6.48 | 1 | $6.48 | -
Wood | $21.24 | 1 | $21.24 | -
Super Glue | $1.97 | 1 | $1.97 | -
LED Display Components | $7.85 | 1 | $7.85 | $2.86
Main Processor Components | 7.14 | 1 | $7.14 | $3.4
MSP430G2553 | $0.00 | 1 | $0.00 | -
TL 792 | $0.00 | 1 | $0.00 | -
TM4C123GH6PM | $0.00 | 1 | $0.00 | -
Paint | $0.69 | 2 | $1.38 | -

## Slide 46: Budget
Sub Total: | $255.52
Shipping: | $35.77
Grand Total: | $291.29

## Slide 47: Work Distribution
Stephen Monn - LED Display Design, Central Processor Design, PCB Design, Sound Processing Design, Rendering Engine Design, Software Design
Omar Alami - Central Processor Design, PCB Design, Power Design, Software Design
Matthew Dworkin - Software Design

## Slide 48: Progress
Main Software (Rendering Engine/ Games)
10% 20% 30% 40% 50% 60% 70% 80% 90% 100%
LED Cube Control (LED Driving/ Display Interface)
Main Controller (Processor/ Power/ Controls)
Stretch Goals (Sound)
Research
Design
Prototype
Testing
Final Package
Overall: 100%

## Slide 49: Overall Difficulties
Very tricky timings!!
IC Coupling
Race conditions
Limited RAM
Heap size allocation
Noise/Cable Shielding

## Slide 50: Questions?