## Slide 1: ManScaper Autonomous Lawnmower
Group 2
Andrew Cochrum
Joseph Corteo
Jason Oppel
Matthew Seth

## Slide 2: Project Goals & Motivation
Remove the chore of mowing your lawn
Create a lawnmower that runs with little to no user interaction
Eliminate the need to detect boundaries using buried cable lines
Create a safe system that avoids obstacles that may be in the path of the mower

## Slide 3: ManScaper Features
Fully electric, rechargeable lawnmower
Boundary detection using computer vision
Object detection to avoid obstacles
Autonomous operation with little to no user interaction required

## Slide 4: ManScaper Design Specifications
Project Design Specs | 
Lawnmower size | 26”x35”x12.5”
Mower location accuracy | ≤ 12”
Forward speed | 1-2 mph
Obstacle detection distance | 2 cm to 3 m
Battery life | ≥ 30 min

## Slide 5: Overall Block Diagram

## Slide 6: Drive Subsystem & Chassis Integration

## Slide 7: Lawnmower Integration onto Existing Chassis
We started with a Greenworks 24 Volt 3-in-1 Cordless Mower

## Slide 8: Lawnmower Integration onto Existing Chassis
Our 1st design had CG issues and was too low to the ground to travel over taller grass

## Slide 9: Lawnmower Integration onto Existing Chassis
Our 2nd design fixed our CG issues and put the mower at an optimal ride height

## Slide 10: Lawnmower Integration onto Existing Chassis
The mower turns and navigates via differential steering achieved by using each motor independently as well as free castoring wheels on the front of the chassis
The mower blade is turned on and off by a simple 25 amp relay via the microcontroller

## Slide 11: Drive Motors/Motor Controller Selection
Since the electric motors were loaned to us by the UCF Robotics Club, motor selection was simple and the motors that were loaned to us provide more than enough power for our application
According to the UCF robotics club the motors each require 25 amps so we needed a motor controller that could handle the current

## Slide 12: Peripheral Sensors

## Slide 13: Infrared vs. Ultrasonic Sensors
 | Infrared sensors | Ultrasonic sensors
Detection range | 2cm – 1m | 2cm – 7m
Beam width | Narrow width | Wide width
Detection issues | Problems in direct sunlight | Poor detection of absorbent materials
Average price | $10-$15 | $30-$40

## Slide 14: Ultrasonic Sensor Comparison
Sensor | Parallax PING))) Ultrasonic Sensor | HC-SR04 | Maxbotix LV-EZ1 | SRF04
Supply Voltage | 5 V | 5 V | 2.5-5 V | 5 V
Supply Current | 30 mA | 2 mA | 3 mA | 30 mA
Range | 2cm-3m | 2cm-0.5m | 0cm-6.45m | 3cm-3m
Frequency | 40 kHz | 40 kHz | 42 kHz | 40 kHz
Size (mm) | 22x46x16 | 20x43x15 | 20x22x16 | 20x43x17
Price | $29.99 | $5.99 | $29.95 | $29.50

## Slide 15: HMC5883L Triple Axis Magnetometer
Used to measure the heading of the lawnmower during operation
Internal measurement scale can be modified via software in case local interference saturates the magnetometer
Disadvantages:
  Inaccuracies when tilted by more than a few degrees from the horizontal
  Sensitive to ferrous materials – must be either shielded or placed at a suitable distance

## Slide 16: RN-XV WiFly Wireless Module
Onboard TCP/IP stack includes DHCP, UDP, DNS, ARP, ICMP, HTTP client, FTP client and TCP
Requires only two pins to communicate with the ATMega328P (RX and TX)
Both the laptop and WiFly module connect to a wireless access point
Once on the same network, a Telnet session will allow for the transfer of location data to the WiFly module

## Slide 17: Microcontroller

## Slide 18: Microcontroller Selection
Specifications taken into consideration for microcontroller selection:
    I/O lines for each component (at least 13 lines total)
      2 lines – HMC5883L Digital Compass
      1 line – PING ))) Ultrasonic Distance Sensor
      2 lines – WiFly RN-XV Wireless Module
      1 line – Sabertooth 2x25 Motor Controller
      4 lines – Quadrature Encoders (2 per encoder)
      2 lines – ADXL345 Accelerometer
      1 line – 25 Amp Solid State Relay
    Widely supported platform
    Reasonable cost

## Slide 19: Microcontroller Selection
Microcontroller choices |  | 
 | MINI-MAX/51-C2 | ATMega328P
Memory | 2 Kbyte of EEPROM memory | 1 Kbyte EEPROM memory
I/O Ports | 32 general purpose I/O pins | 23 programmable I/O lines
Additional Advantages | Analog/Digital Converter | Analog/Digital Converter
Programming | In-circuit programming/ debugging | Program is flashed through UART (IC programming is possible through burned boot loader)
Cost | $53.00 | $29.99

## Slide 20: Microcontroller Selection
ATMega328P chosen for this design
  Wide selection of libraries available for each component
    Reduces time spent programming
  23 ports available for components (I/O lines)
  Arduino IDE allowed for C/C++ programming
  Reasonable cost
  Readily available at local vendors

## Slide 21: Power Subsystem

## Slide 22: Component Power Requirements
Component | Voltage | Max Current Draw
Drive motors | 24 V | 3 A (each)
Microcontroller | 5 V | 12 mA
Ultrasonic sensor | 5 V | 35 mA
Wi-Fly module | 3.3 V | 38 mA
Digital compass | 3.3 V | 100 μA
Total maximum current draw of ≈ 6.09 A |  | 

## Slide 23: Battery Selection
Existing battery used for blades
  Maximizes blade run time
Desired a ½ hour of minimum run time
Low cost
Two UB12350 12V / 33Ah sealed lead-acid batteries in series
  Same battery is used to drive the commercial electric wheelchair that uses our DC motors

## Slide 24: Linear vs. Switching Regulators
85 mA regulated current draw
Pout = 5V * 85mA = 425mW
  LM2825 1A switching regulator (24 pin DIP package)
 | Linear regulator | Switching regulator
Efficiency (η) | ≈ 41.7% | ≈ 80%
Power dissipation Pd = Pout / η - Pout | 425/0.417 – 425 = 0.59 W | 425/0.8 – 425 = 0.11 W

## Slide 25: Location Subsystem

## Slide 26: Computer Vision: General Setup
Webcam will be mounted on top of support structure to provide a high enough elevation to survey the entire area

## Slide 27: Computer Vision Software: Running Segmentation in SimpleCV
Camera takes a raw image
Previous images are averaged and then subtracted from the current image
  This results in a binarized image that only shows pixels that have changed
  The binarized image is dilated to make the blobs more pronounced
Program then stores blobs into a feature set
  Blobs are filtered based on pixel distance from the previous blob
  Ensures that the program is tracking the mower and not another moving object

## Slide 28: Computer Vision: Computing Boundaries

## Slide 29: Overall Schematic

## Slide 30: PCB Design

## Slide 31: PCB Design

## Slide 32: Responsibility Distribution
 | Andrew | Jason | Joe | Matt
Chassis fabrication | X |  |  | 
Drive subsystem | X |  |  | 
Computer vision |  | X | X | 
Obstacle avoidance |  | X | X | 
Power subsystem | X | X |  | 
Mower navigation |  | X | X | 
PCB design | X |  |  | 
Administrative | X | X | X | X

## Slide 33: Budget
Part | Manufacturer | Quantity | Unit Price | Net Price
25222 20-Inch 24-Volt Cordless Lawn Mower | Greenworks | 1 | $369.00 | $150.00 (used)
Ideapad Z560 Laptop | Lenovo | 1 | $597.00 | $0.00 (used)
DC brushed motor with gearbox and wheel | X | 2 | $181.64 | $0.00 (donated)
ATMega328 with development board for testing | Atmel | 4 | $29.99 | $119.96
PING))) Ultrasonic Distance Sensor | Parallax Inc. | 1 | $29.99 | $29.99
Sabertooth 2x25 V2 motor controller | Sabertooth | 1 | $124.99 | $124.99
HMC5883L Triple Axis Magnetometer | Sparkfun | 1 | $14.95 | $14.95
Lifecam HD-5000 Webcam and USB extension | Microsoft | 1 | $34.99 | $34.99
12V Sealed Lead Acid Battery 33-35Ah | Batteries.com | 2 | $59.99 | $119.98
LM2825-5.0 fixed output switching regulator | TI | 1 | Free sample | $0.00
LM2825-3.3 fixed output switching regulator | TI | 1 | Free sample | $0.00
Breakout board for XBee module | Sparkfun | 1 | $2.95 | $2.95
RN-XV WiFly Wireless Module | Roving Netwks | 1 | $34.95 | $34.95
PCB 2 Layer Full Spec | Adv Circuits | 1 | $77.00 | $77.00
Various PCB Components | X | X | $60.00 | $60.00
DIR-655 Wireless-N Router | D-Link | 1 | $94.99 | $0.00 (donated)
25A Solid State Relay | Shenlan | 1 | $25.00 | $25.00
Drive subsystem fabrication supplies | Home Depot | X | $30.00 | $30.00
Webcam telescopic platform building supplies | Home Depot | X | $100.00 | $100.00
 |  |  | Total Price | $924.76

## Slide 34: Issues
DC motor specs were unknown
Fabrication issues
  Original angle iron was not strong enough
  CG issues
  Platform was too low for taller grass
Compass needed offset for calibration
Dead reckoning mapping in combination with computer vision
PING))) sensor false positives
Color/hue segmentation in computer vision

## Slide 35: Questions