## Slide 1: GROUP #4 Chris Carmichael, EE Ismael Rivera , CpE Journey Sumlar, EE Warayut Techarut, CpE
T-100 WATCHDOG

## Slide 2: Project Introduction
Detect Motion
Track Movement
Alert User
Remote Control
Streams Video
Camera View

## Slide 3: Project Goals
  System Integration
  Motor Control
  Computer Vision
  Wireless Communication
  Power Control

## Slide 4: Requirements
Autonomous
Detect Motion
Wireless Communication
Video Streaming

## Slide 5: Specifications
Feature | Measurement
Dimension | 12” x 8”
Operating Range | 25 ft
Power Supply Voltage | 14.4 v
Maximum Weight | 20 lbs
Minimum Acceleration | 1 ft/s2
Maximum Speed | 3 ft/s
Battery Life | 3 hrs
Recharge Time | < 4 hrs

## Slide 6: Block Diagram

## Slide 7: System on Chip (SoC)

## Slide 8: Raspberry Pi vs BeagleBone Black
Raspberry pi
$35.00
700 MHz ARM1176JZFS
512 MB SDRAM @ 400 MHz
8 GPIO Pins
Beaglebone black
$45
1GHz TI Sitara AM3359 ARM Cortex A8
512 MB DDR3L @ 400 MHz
65 GPIO Pins

## Slide 9: Microcontroller & Development Board
ARM Cortex A8
TI Sitara AM3359
BeagleBone Black

## Slide 10: Microcontroller & Development Board

## Slide 11: Microcontroller & Development Board

## Slide 12: Operating Systems
Debian
  Default OS
ArchLinux|ARM
  Most Lean
Windows Embedded
  Most Integrated

## Slide 13: Wi-Fi

## Slide 14: Wi-Fi
Edimax EW-7811Un
  IEEE 802.11b/g/n
  Compatible with Linux
  Small size
  Internal Antenna
  WEP/WPA/WPA2/WPS Compatible
7.1 mm
14.9 mm
18.5 mm

## Slide 15: Computer Vision

## Slide 16: Open Source Libraries
Robot Operating system (ROS)
Implementations for specific tasks.
Not as big as OpenCV.
Requires OpenCV for certain algorithms.
Open Source Computer Vision Library (OpenCV)
C++ and JAVA implementations available.
Compatible with multiple distributions of Linux.
Large amount of tutorials and support community .

## Slide 17: Computer Vision - OpenCV
  Detect movement
  Recognize and track a moving person
OpenCV 2.4.2
  Optimized computer vision functions and algorithms
  Built-in Object Detection and Tracking functions
  ARM Support
  Performance varies on functions being utilized.

## Slide 18: Computer Vision State Diagram

## Slide 19
0 – 212 LEFT | 213 – 425 STAY | 426 – 640 RIGHT
640
480

## Slide 20: Server & Streaming

## Slide 21: Server & Streaming
Node.js
  Enable internet HTTP communication
  Web GUI (Optional)
  Lightweight on resources under load
UDP (User Datagram Protocol)
  JAVA Implementation (Android Compatible)
  Always listening for incoming commands from mobile phone
  Very lightweight on resources
  Port specific
Chart: Server Benchmark
| Apache | Open LiteSpeed | Nginx | Node.js
 | 42.4 | 47.1 | 25.3 | 12.1

## Slide 22: Server & Streaming
MJPG-Streamer
  Streams images from a folder over the internet
  Stream and Snapshot functions available
  Android compatible stream
  Low resource usage

## Slide 23: Streaming State Diagram

## Slide 24: Webcam

## Slide 25: Webcam
Microsoft - LifeCam Cinema
  USB 2.0 Connectivity
  Linux Compatible
  Multiple picture/video resolutions available
Notes: Compare with others

## Slide 26: Mobile Application

## Slide 27: Mobile Application
  Support Android 4.0 and newer versions
  SQLite Database to store user credentials
  Control vehicle remotely
  View a live video feed
  Store snapshot on the device

## Slide 28: Mobile Application State Diagram

## Slide 29: Mobile Application
Registration Activity
  Allow user to register a username/password combination.
  Store cell phone for SMS and MMS alerts.
    Supports: AT&T, Sprint, T-Mobile, Verizon, MetroPCS, Boost Mobile, Straight Talk.
  Store email for email alerts.
  Send SMS, MMS, and Email address to external server via PHP Post/Get method.

## Slide 30: Mobile Application
Login Section
  Allows user to register/login
  Only authorized users will have access
  Performs an Internet Check

## Slide 31: Mobile Application
Control Section
  View live video feed
  Control robot with virtual joystick
  Store snapshot

## Slide 32: Mobile Application
Gallery Section
  View snapshots stored on device
  Share via Email/MMS

## Slide 33: Motor Controller, Motors, & Wheels

## Slide 34: Mecanum Wheels
Notes: Add Diagrams

## Slide 35: Mecanum Wheels
Notes: Add Diagrams

## Slide 36: Mecanum Wheels
Notes: Add Diagrams

## Slide 37: Mecanum Wheels
Vex Robotics Mecanum Wheels
  Affordability
    $59.99 4 pack
  Diameter: 4 in.
  Thickness: 2 in.

## Slide 38: Platform
Perforated Aluminum – Lightweight
2 pounds with wheels included
Easily Adjustable
12 in.
8 in.

## Slide 39: Motor
VEX 2-Wire motor 393
VEX 2-Wire motor 393 | Requirements | Specs-Low Speed | Specs- High speed
Price | < $20 | $14.99 | $14.99
RPM’s | 130 | 100 | 160
Torque | 1.3 Nm | 1.67 Nm | 1.04 Nm
Weight | < .5 lbs | .2 lbs | .2 lbs
Stall current |  | 4.8 A | 4.8A
Max Power | All measured at 7.2 V | 34.56 W | 34.56 W
2 in.
1.5 in.
1 in.

## Slide 40: H-Bridge Circuit

## Slide 41: H Bridge Components
IRF 9530 P-Channel | IRF 530 N-Channel | BC547
100 Vds | 100 Vds | 47 V Breakdown
12 A | 14 A | 100 mA
$1.29 | $1.03 | $0.20
10 K OHM Current Limiting Resistors

## Slide 42: Controller Budget
Component | How many | Price per unit | Total
MSP430G2552 | 4 | $2.79 | $11.16
IRF9530 | 8 | $1.29 | $10.32
IRF530 | 8 | $1.03 | $8.24
BC547 | 32 | $0.20 | $6.40
Capacitor(100nF) | 4 | $.05 | $0.20
Resistor (10k) | 40 | $.04 | $1.60
Total: (without pcb) |  |  | $37.92

## Slide 43: Motor Controller- PCB
Specifications
3”x3”
Thick Traces for high current lines
2 layer
Oshpark, $5/sq in. 3 PCB’s per order.

## Slide 44: USB Power Hub

## Slide 45: USB Power Hub
BeagleBone Black only has 1 USB port.
2.0 USB Ports
Input voltage is 3-5V
Constant power to each USB port
Weight 8 oz.
6 in.
.5 in.
1 in.

## Slide 46: Power Management & Battery

## Slide 47: Single Power Supply or Multi Power Supply?
  Multi power supply to power all components
  Battery Characteristics
    High discharge Rate
    No/low Memory Effect
    Light Weight
    High Capacity
    Price Effective
    High Nominal Voltage

## Slide 48: Battery Specifications
Top three candidates for batteries
Most important aspects are Capacity, Discharge Rate, and Voltage
Model | 31604 | 31038 | 18650
Brand | Tenergy | Tenergy | Supower
Capacity (mAh) | 1600 | 4400 | 2200
Voltage (V) | 7.4 | 14.8V | 7.4
Weight (Ib) | 0.2 | 1.2 | 0.2
Discharge Rate (C) | 20 (32 A) | 25 (60A) | 2.5 (5.5A)
Price ($) | 24.5 | 59.99 | 17.99
Chemistry | Lipo | Li-on | Li-on

## Slide 49: Battery Selection Motor Controller
Tenergy 14.8V 4400mAh Battery
Weighs the most but supply the most current out of the batteries.
Expected Battery Life needs to be at least 3 Hours
Model | 31604 | 31038 | 18650
Brand | Tenergy | Tenergy | Supower
Capacity (mAh) | 1600 | 4400 | 2200
Voltage (V) | 7.4 | 14.8V | 7.4
Weight (Ib) | 0.2 | 1.2 | 0.2
Discharge Rate (C) | 20 (32 A) | 25 (60A) | 2.5 (5.5A)
Price ($) | 24.5 | 59.99 | 17.99
Chemistry | Lipo | Li-on | Li-on

## Slide 50: Battery Selection Microcontroller
USB Powered Battery
7.4V Lithium Ion 6600mah
Two output ports
  5V at 1A
  5V at 2A
Powers off automatically once the devices are disconnected.

## Slide 51: Battery Charger
Tenergy TLP-2000 Smart Charger
  Built in Balancer
  Price $25.99
  Powers both Lion and LIPO batteries.
  Led Indication Status on when battery is charging and when the battery is fully charged
  Cuts off once battery is fully charged.

## Slide 52: SPST 12VDC/30A Switch
Rated at 12V 30A
Red LED illuminates while on
Great to Conserve Battery life
Nickel plated brass
1.25”
2.5”

## Slide 53: Power Requirements
Items | Voltage input needed | Current input needed
BeagleBone Black | 5 V | 2 A
Motor Controllers | 10 V | 16 A
Conventional Webcam | 3 V | <500 mA
MSP 430 | 3.3 V | .5 mA
Wi-Fi Adapter | 3 V | <500 mA
USB Power Hub | 3-5 V | 1.5 A

## Slide 54: Power System

## Slide 55: Voltage Regulators
LM 338
Output Voltage range is 1.2V to 32V
Output current Max 5A
Output voltage is 10V
Heatsinks Needed
2 regulators
LM 350
Output Voltage range is 1.2V to 32V
Output current Max 2A
Output voltage is 3.3V
Heatsinks Needed
1 regulator

## Slide 56: Work Breakdown
Task | Ismael Rivera | Warayut Techarut (Wye) | Journey Sumlar | Chris Carmichael
Motor Controller |  |  |  | X
Power Management |  |  | X | 
Server | X |  |  | 
Computer Vision | X | X |  | 
Mobile Application | X |  |  | 
Microcontroller Communication |  | X |  | 

## Slide 57: Budget & Finance
Part Name | Quantity | Price (each) | Total
Wifi USB Adapter | 1 | $5.99 | $5.99
MicroSD Card | 1 | $7.99 | $7.99
USB AC Powered Hub | 1 | $7.99 | $7.99
Motor | 5 | $14.99 | $74.95
Mecanum Wheels | 1 | $59.99 | $59.99
Robot Frame kit | 1 | $79.99 | $79.99
Motor controller PCBs | 2 | $43.95 | $87.90
Motor Controller Parts | 1 | $46.00 | $46.00
22 guage wire set | 1 | $20.00 | $20.00
Wire connectors | 1 | $40.00 | $40.00
Barrel jack connectors | 2 | $2.95 | $5.90
USB Battery | 1 | $29.95 | $29.95
Battery + Charger | 1 | $88.55 | $88.55
BeagleBone Black | 1 | $62.71 | $62.71
Miscellaneous |  |  | $50
 |  | Total | $667.91
 |  | Over budget | $42.54

## Slide 58: Issues
Low performance for OpenCV (1-2 frames per second)
  Driver not fully compatible
  Faster Processor
UCF Network Restrictions
Time constraints
Budget

## Slide 59: Project Process

## Slide 60: Project Process

## Slide 61: GROUP #4 Chris Carmichael Ismael Rivera Journey Sumlar Warayut Techarut
Questions?