## Slide 1
Fire Detection and Eradication
Bernadeau Charles
Matt Erdelac
Erik Ferreira
Armin Sadri
Group 13

## Slide 2: Project Overview
HeatSeekr addresses issues plaguing the current fire extinguishing methodology.
Minimizes the amount of additional damage caused by traditional fire systems.
Efficient and accurate without human interaction

## Slide 3: Primary Goals and Objectives
Be able to detect the beginning stages of a fire.
Extinguish flames with concentrated water.
Be fully independent and autonomous.

## Slide 4: Design Specifications
Criteria | Specification
Fire Detection Range | Up to 20 feet
Fire Detection Response Time | Under 30 seconds
Navigational Response Time | Travel 40 feet under 1 minute
Water Extinguisher Range | Distance of 5 feet
Standby Response Time | Operate after sleeping for 2 hours
Weight | Under 30 lbs
Total Size | Under 2ft x 2ft x 2ft

## Slide 5: Flowchart
Extinguishing
µC
Master
µC
Navigation
µC
Fire Detector
Aiming Motors
Extinguisher
LCD Screen
Bluetooth
Line Follower
Drive Motors
Water Level Sensor
Wireless
µC
Bluetooth
Fire Detector
I2C
I2C
UART
UART

## Slide 6: Fire Detection
Extinguishing
µC
Fire Detector
Aiming Motors
Extinguisher
Water Level Sensor

## Slide 7
Three initial choices: IR Camera, IR Thermometer, and Hamamatsu UVTron
Main specification: feasible and efficient to incorporate on rover and wireless probe
Fire Detection

## Slide 8
Fire Detection - Methods
 | IR Camera | IR Thermometer | UVTron
Functional Essence | IR sensitive image | IR value for a point | UV sensitive transistor
Interface | UART | SPI | µC Pin
FOV Control | Medium – Software | None – point source | Shroud – Naturally Omni
Processing | OpenCV Contour Match | Array Max Value Search | Frequency Counter
Processing Requirement | Very High | Low | Low
Scanning Requirement | X plane motor | X-Y plane motor | X plane motor/omni
Detection Speed | Slow – 1 minute per degree | Slow – 1 minute per x-parallel | Fast – 1 degree per second
Detection Range | ~15 feet | Less than 7 feet | 20+ feet
Voltage Requirement | 5V | 5V | 12V
Current Consumption | 90mA | 5mA | 4mA
Cost | $49.95 | $99.50 | $84.90*

## Slide 9
 | UVTron
Functional Essence | UV sensitive transistor
Interface | µC Pin
FOV Control | Shroud – Naturally Omni
Processing | Frequency Counter
Processing Requirement | Low
Scanning Requirement | X plane smotor/omni
Detection Speed | Fast – 1 degree per second
Detection Range | 20+ feet
Voltage Requirement | 12V
Current Consumption | 4mA
Cost | $84.90*
Fire Detection - UVTron

## Slide 10
Fire Detection - UVTron

## Slide 11
Fire Detection - Render

## Slide 12: Fire Extinguisher
Extinguishing
µC
Fire Detector
Aiming Motors
Extinguisher
Water Level Sensor

## Slide 13
Two considered methods: ABC dry chemical and water cannon
Main specification: Ease of testing and implementation
Fire Extinguisher

## Slide 14
Comprised of water tank, pump, and hose
Appropriate for Class A fires
Advantages: Ease of activation and testing - $83.95
Disadvantages: Cannot handle B and C fires, cumbersome aiming
Fire Extinguisher – Water Cannon

## Slide 15
Fire Extinguisher – Water Cannon
Implemented
Firing Pattern
For-loop controlled
alternation of motors

## Slide 16
Navigation
µC
Line Follower
Drive Motors
Line Follower

## Slide 17
Line Follower
Based on CNY70 Optical Transistor
Output depends on reflection of IR light
Array of CNY70s feeds into comparator
Comparator outputs logic level Boolean response

## Slide 18
Line Follower - Schematic

## Slide 19: Line Follower - Navigation
010
Both motors on
011
Left motor on, right motor off

## Slide 20
Line Follower – PCB Representation

## Slide 21
Extinguishing
µC
Master
µC
Navigation
µC
Fire Detector
Aiming Motors
Extinguisher
LCD Screen
Bluetooth
Line Follower
Drive Motors
Water Level Sensor
Wireless
µC
Bluetooth
Fire Detector
I2C
I2C
UART
UART
Drive Motors

## Slide 22: Tread Kit
Criteria | Specification
Length | 2 chains of up to 32.75 in
Tread Width | 1.5 in
Tread Weight | 12 inches weights 0.532 lbs.
Tread Drive Diameter | Approx. 2.375 in
Material | Delrin Plasitc
VEX Robotics Tank Tread Kit

## Slide 23: Drive Motor
 | GHM-13 | PGHM-02
Reduction Ratio | 50 : 1 | 91: 1
Voltage | 12 Vdc | 12 Vdc
RPM | 152 | 65
Outside Diameter | 37 mm | 35 mm
Stall Torque | 231.5 oz-in | 388.85 oz-in
Weight | 7.28 oz | 8.90 oz
Cost | $29.95 | $37.95

## Slide 24: Motor Driver
 | L293DNE
Supply Voltage | 4.5 V to 36 V
Output Current | 1 A per channel
Peak Output Current | 2 A per channel
Operating Temperature | -0°C ~ 70°C
Cost | Free

## Slide 25: Drive Motors – Schematic

## Slide 26
Extinguishing
µC
Master
µC
Navigation
µC
Fire Detector
Aiming Motors
Extinguisher
LCD Screen
Bluetooth
Line Follower
Drive Motors
Water Level Sensor
Wireless
µC
Bluetooth
Fire Detector
I2C
I2C
UART
UART
Aiming Motors

## Slide 27: Aiming
Extinguishing
µC
Aiming Motors
Fire Detector
Extinguisher
Water Level Sensor

## Slide 28: Stepper Motors
 | PM42M | HT23-180-8 | 39BYG302
Step Angle | 7.5 ° | 1.8 ° | 1.8 °
Drive Voltage | 24 V | 12 V | 12 V
Current / Phase | 0.5 A | 2.5 A | 0.32 A
Coil Resistance | 80 Ωs unipolar or 6 Ωs bipolar | 1.23 Ωs unipolar or 0.62 Ωs parallel | 15.0 Ωs
Torque | 4 N-cm | 13 N-cm | 1 N-cm
Cost | $7.95 | $33.95 | $12.95

## Slide 29: Bipolar Stepper Motor Driver
 | DRV8811
Vs (Min) (V) | 5
Vs (Max) (V) | 38
RMS Output Current (A) | 1.4
Peak Output Current (A) | 1.9
# of Full Bridges | 2
Operating Temperature Range (C) | -40 to 85
RDS(ON) (HS + LS) (mOhms) | 1000
Current Regulation Levels | 8
Additional Features | 1/8 Microstepping P2P w/ DRV8818
# of half-bridges | 4
Cost | Free

## Slide 30
Stepper Motor - Schematic

## Slide 31
Extinguishing
µC
Master
µC
Navigation
µC
Fire Detector
Aiming Motors
Extinguisher
LCD Screen
Bluetooth
Line Follower
Drive Motors
Water Level Sensor
Wireless
µC
Bluetooth
Fire Detector
I2C
I2C
UART
UART
Microcontrollers

## Slide 32: Microcontrollers
 | MSP430G2553 | ATmega328
Voltage Range | 1.8 V to 3.6 V | 1.8 V to 5.5 V
Max. Operating Frequency | 16 MHz | 20 MHz
Power Consumption | Active: 230μA at 1MHz, 2.2V Standby: 0.5 μA | Active: 0.2mA Standby: 0.75 μA
Timer | Two 16-bit timers | Two 8-bit, One 16-bit
I/O pins | 20 or 28 package | 23
Memory | 16 kB | 32 kB
RAM | 512 Bytes | 512 Bytes
Cost | Free | $2.88

## Slide 33: Master Schematic

## Slide 34: Navigation Schematic

## Slide 35: Extinguisher Schematic

## Slide 36
Extinguishing
µC
Master
µC
Navigation
µC
Fire Detector
Aiming Motors
Extinguisher
LCD Screen
Bluetooth
Line Follower
Drive Motors
Water Level Sensor
Wireless
µC
Bluetooth
Fire Detector
I2C
I2C
UART
UART
Mainboard IC Communication

## Slide 37: Mainboard IC Communication
I2C
  UART is chip-to-chip
  SPI required too many GPIO pins
Master processor will handle all communication of the rover
  Is there a fire?
  Are we moving?
  Have we arrived?

## Slide 38
Extinguishing
µC
Master
µC
Navigation
µC
Fire Detector
Aiming Motors
Extinguisher
LCD Screen
Bluetooth
Line Follower
Drive Motors
Water Level Sensor
Wireless
µC
Bluetooth
Fire Detector
I2C
I2C
UART
UART
Wireless

## Slide 39: Wireless
 | RN-171 | RN-42 | CC2520
Specification | 802.11 b/g | 802.15.1 V2.1 | 802.15.4
Common name | Wi-Fi | Bluetooth | Zigbee
Operating voltage | 3.3 V | 3.3 V | 3.3 V
Current Consumption (Tx) | 120 mA | 30 mA | 25.8 mA
Current Consumption (Sleep) | 4 µA | 26 µA | <1 µA
Interface | UART, SPI | UART, SPI | SPI
Antenna | External | On-board trace | External
Cost | $26.25 | $19.14 | $6.05

## Slide 40: RN-42
UART - ‘invisible wire’
Commands vs Data
  Device always assumes data
  Sending the ‘connect’ command:
    Send three ASCII ‘$’ – Enter command mode
    Send ASCII ‘C,’ – ‘connect’ command
    Send three ASCII ‘-’ – Leave command mode
$
$
$
C,
-
-
-

## Slide 41
Extinguishing
µC
Master
µC
Navigation
µC
Fire Detector
Aiming Motors
Extinguisher
LCD Screen
Bluetooth
Line Follower
Drive Motors
Water Level Sensor
Wireless
µC
Bluetooth
Fire Detector
I2C
I2C
UART
UART
Remote Probe

## Slide 42: Remote Probe
Detect fires away from the rover
UVTron, MSP430G2553, RN-42
Bluetooth Master
  Rover has the Bluetooth slave module
Ultra low power
  µC sleeps in LPM4 – 0.1 µA @ 25°C
  RN-42 not connected
  4.5 mA

## Slide 43: Remote Probe Logic Flowchart
µC enters LPM4
Pulse from UVTron
µC enters Active Mode
Determine if fire is present
Fire?
RN-42 connects
‘Fire present’ sent
RN-42 disconnects
Yes
No

## Slide 44: Remote Probe Schematic

## Slide 45
Extinguishing
µC
Master
µC
Navigation
µC
Fire Detector
Aiming Motors
Extinguisher
LCD Screen
Bluetooth
Line Follower
Drive Motors
Water Level Sensor
Wireless
µC
Bluetooth
Fire Detector
I2C
I2C
UART
UART
LCD Screen

## Slide 46: LCD Screen
Hitachi MED100-DSPL
40 characters per line, 2 lines
Using Nikosapi’s HD44780 Library for the MSP430
Displays status messages

## Slide 47: Water Tank
12”x 7”x 6” water tank with ¼” thickness.
Ultraviolet-Resistant Clear Extruded Acrylic Sheets
Additional supports inserted inside.
Able to support a maximum of 2.18 gallons with a maximum weight of 16.68 lbs
Sheets attached with Weld-On #4 Acrylic Adhesive

## Slide 48
Extinguishing
µC
Master
µC
Navigation
µC
Fire Detector
Aiming Motors
Extinguisher
LCD Screen
Bluetooth
Line Follower
Drive Motors
Water Level Sensor
Wireless
µC
Bluetooth
Fire Detector
I2C
I2C
UART
UART
Water Level Sensor

## Slide 49: Water Level Sensor
Used to determine water level
Essentially a “ground detection” sensor
Pseudo-code for the water level sensor

## Slide 50: Chassis
12.5 x 12.5 inches.
Tank supported by center 12 x 6 inch support and L brackets.
Tank treads have support guards around them that also double for handles.

## Slide 51: Power Requirements
 | Operating Voltage | Current Consumption | Power Consumption
Microcontroller | 3.3 V | 0.5 mA | 1.65 mW
Water level Sensor | 3.3 V | 0.3 mA | 0.99 mW
Line Following Sensor | 3.3 V | 3 mA | 9.9 mW
Wireless Module | 3.3 V | 30 mA (Tx) | 99 mW (Tx)
Stepper Motors | 12 V | 300 mA | 3.6 W
Drive Motor | 12 V | 80 mA | 960 mW
UVTron | 12 V | 4 mA | 48 mW
Water pump | 12 V | 2.5 A | 30 W

## Slide 52: Power Components
Tenergy 22.2V 7800mAh li-po battery pack
Physical switch to turn HeatSeekr on and off, throw in reverse for charging.
3.3 and 5 volt switching regulators (Murata Power Solutions 78SR-3.3/2)
12 volt switching regulator (Custom)

## Slide 53
3.3 V Switching VR
12 V Switching VR
MSP430
Bluetooth module
Tenergy 22.2V
Drive motors
UVTron
Water Pump
5 V Switching VR
Power Flow Chart
LCD Screen
Stepper Motors

## Slide 54: Power Supply Schematic

## Slide 55: Battery Specifications Summary
Specifications | Ni-MH | Ni-Cd | Li-Po | Li-ion
Energy density (W-hr/kg) | 70-90 | 40-60 | 130-200 | 100-160
Capacity (Amp-hr) | 2.4 | 1 | 12.6 | 2.8
Internal resistance (mΩ) | 200-300 | 100-200 | 200-300 | 100-200
Nominal voltage (V) | 1.2 | 1.2 | 3.7 | 3.6
Discharge Rate | Flat | Flat | Flat | Flat
Recharge cycle | 600-1000 | 500-700 | >1000 | > 600
Disposal | Recyclable | Non-degradable | Recyclable | Recyclable
Charge/discharge efficiency | 66% | 70-90% | 99.80% | 80%-90%
Cost ($/Whr) | 2.75 | 2 | 2.8-5 | 2.5

## Slide 56: Budget and Finance
Part | Cost per unit | Required | Total Cost
Hamamatsu UVTRON Flame Sensor R2868 | $35.95 | 2 | $74.00
C3704 Hamamatsu UVTRON Board | $49.94 | 2 | $62.00
TOPSFLO Micro Gear pump | $15.00 | 1 | 15
1.0 kg/cm Nema 16 Step Motor- 39BYG302 | $12.95 | 2 | $25.90
Bipolar Stepper Motor DriverDRV8811 | $4.67 | 2 | Free*
Vex Robotics Tank Tread Kit | $29.99 | 1 | $29.99
Planetary Gear Motor PGHM-02 | $37.95 | 2 | $75.90
Reflective Optical Phototransistor | $0.76 | 4 | $3.04
Part | Cost per unit | Required | Total Cost
3.3V / 5V Switching Regulator | $13.18 | 2 | $26.36
2-layer PCB board | $33.00 | 1 | $33.00
Plexiglas | $9.03 | 6 | $54.18
MSP430G2553 | $2.50 | 4 | Free*
Chassis | $25.00 | 1 | $25.00
Wood framing | $20.00 | 1 | $20.00
Misc. screws/nuts | $75.00 | 1 | $75.00
Battery | $112.00 | 1 | $112.00
Charger | $27.00 | 1 | $27.00
Weld on | $30.30 | 1 | $30.30
12 volt regulator | $15.00 | 1 | $15.00
RN42-I/RM | $19.14 | 2 | $38.28
 |  | Total: | $741.95

## Slide 57: Labor Distribution
 | Power | Chassis | Sensors | Motors | Microcontroller | Wireless | Navigation
Bernadeau Charles | X | X |  |  |  |  | 
Matt Erdelac |  |  | X |  | X | X | 
Erik Ferreira |  | X |  | X | X |  | 
Armin Sadri |  | X | X |  |  |  | X

## Slide 58: Issues
Stepper Motors heating up.
Water distribution from sudden acceleration and deceleration.
Purchased 12V regulator was unable to supply the necessary current to run the pump.

## Slide 59: Questions?