## Slide 1: Energy Efficient Location Sensing
Brent Horine
March 30, 2011

## Slide 2: Citation
Jeongyeup Paek, Joongheon Kim, Ramesh Govindan, “Energy-Efficient Rate-Adaptive GPS-based Positioning for Smartphones,” In Proc. Of the 8th International Conference on Mobile Systems, Applications, and Services (MobiSys), 2010, pp. 299-314.
Authors are affiliated with the Embedded Networks Laboratory, Computer Science Department, University of Southern California

## Slide 3: Motivation
Many smartphone applications require location services
GPS is very power hungry (0.37 W on Nokia N95)
Not all applications require the accuracy that GPS provides
Nor do they all the most recent position
In urban canyons, GPS is all that accurate anyway
A system which can tradeoff position accuracy with power consumption could improve battery life with no discernable sacrifice in application usability

## Slide 4: RAPS
Rate Adaptive Positioning System for smartphones

## Slide 5: Duty Cycle Impact of GPS
But how do you match up the duty cycle with user mobility and ensure a bounded error?

## Slide 6: Significant Contributions
Cheap (computationally) algorithm to infer whether and when GPS activations are necessary
Integrates many previously disclosed techniques in a unified platform

## Slide 7: Algorithm Description
Learn user velocities at a given location and time of day
Correlate to accelerometer readings to estimate consistency
Use this information to predict the likelihood of a position update requirement
Senses signal strength and tower ID and queries history for likelihood of successful fix info
Checks local Bluetooth radios for a opportunistic location fix

## Slide 8: General Experimental Results
Nokia N95 smartphones deployed on campus
3.8X better lifetime than continuous GPS
1.9X better lifetime than periodic GPS scheme with comparable error rate

## Slide 9: GPS Inaccuracies in Urban Area
1 week data logger at 1 sec interval
Shows ghost traces and errors

## Slide 10: Average and Max Errors

## Slide 11: GPS Error Budget
Error Source | Error Budget | Units
Ionospheric effects | +/-5 | meter
Orbit shifts | +/-2.5 | meter
Satellite clock errors | +/-2 | meter
Multipath effects | +/-1 | meter
Tropospheric effects | +/-0.5 | meter
Rounding errors | +/-1 | meter
Assumes 4 satellites in view. Degrades significantly with only 3 in sight.

## Slide 12: GPS errors
Change in GPS fix every 180 seconds
Mostly measuring mobility
Self reported accuracy estimates

## Slide 13: Update Interval vs Delta-fix for periodic updates

## Slide 14: Accelerometer Activity Indicator

## Slide 15: Power Consumption of Accelerometer

## Slide 16: Accelerometer Duty Cycle Analysis
Setting duty cycle at 12.5% reduces power consumption by 8X for 0.01W

## Slide 17: Framework for User Mobility History

## Slide 18: Usefulness of Cell ID?

## Slide 19: Futility of using RSSI to Estimate Movement

## Slide 21: Experiment Matrix

## Slide 22
6 phones in one bag, carried by author for almost 2 days
No other apps running on phones
Measure battery life

## Slide 23: Lifetime

## Slide 24: Event Timeline: BPS

## Slide 25: Celltower Blacklist Effectiveness

## Slide 26: Average GPS Interval

## Slide 27: Average Power Consumption

## Slide 28: Median delta-GPS-Fix

## Slide 29: Avg Position Uncertainty vs GPS Duty Cycle

## Slide 30: Success Ratio Relative to Periodic GPS vs Duty Cycle

## Slide 31: Power Consumption of WPS
WPS – WiFi Positioning Service
Is RAPS compatible?

## Slide 32: Assisted-GPS Analysis

## Slide 33: Errors vs Phone Comparison

## Slide 34: Reflections
Many of these researchers fail to take advantage of the significant literature on GPS inaccuracies and instead take new measurements
They also consider Google Maps to be ground truth, instead of using survey markers
In my professional work with GPS, I routinely smoothed the data with a moving average filter over e.g. 10 samples. I don’t know what is done in the OS, but this is generally required when dealing directly with the e.g. GPRMC sentences

## Slide 35: More Reflections
A statistical approach to design of the experiment (a.k.a. Box & Hunter or Taguichi) would have produced much more confidence in the empirically derived conclusions for the same effort
Industry versus Academic (most of their conclusions are well known to an engineer working in the GPS field)

## Slide 36: Questions & Comments