## Slide 1: EnviroSense
Jonathan Mohlenhoff
EEL6788 - Team 16
04/20/2011

## Slide 2: Introduction
Hardware project focused on interfacing external sensors to mobile devices
Expands variety of sensors available to developers for urban sensing applications
Current sensors available on mobile devices are few, restricted to UI and location functionality:
  Multi-touch, accelerometer, compass, GPS, microphone, camera
Adding new sensors allows researchers to expand on experiments

## Slide 3: Description
Add environmental sensors to iOS device
Custom designed PCB that interfaces between iOS device and sensors
Ability to sense:
  Temperature
  Humidity
  Barometric Pressure
  Carbon Monoxide (CO)
  Carbon Dioxide (CO2)
  Ozone (O3)
  General Air Quality

## Slide 4: Related Work
Common Sense: Mobile sensing for community action
  http://www.communitysensing.org/
  Self-contained, built in:
    GPRS Modem, GPS, Bluetooth, sensors, battery
Mote Platform
  http://www.eecs.berkeley.edu/~prabal/projects/epic/
  Large developers community

## Slide 5: More Related Work
The Urban Pollution Monitoring Project
  http://www.equator.ac.uk/index.php/articles/563
  Self contained system
  Older system
Air: Preemptive Media Project
  http://www.pm-air.net/index.php

## Slide 6: Hardware Design
Sensors
  SENSIRION - SHT15
    Temperature and Humidity
    Two Wire Interface (TWI)
  VTI Technologies – SCP1000
    Temperature and Barometric Pressure
    Serial Peripheral Interface (SPI)
  MQ-7 CO Gas Sensor
  MG811 CO2 Gas Sensor
  MQ135 Air Quality Sensor
  MQ131 O3 Gas Sensor

## Slide 7: Hardware cont.
Required custom printed circuit board
  Microcontroller Atmel Atmega328P to interface to sensors and iPad
  Connects to iPad via 30 pin connector
    Tx – pin 12, Rx – pin 13
  Powers off of 3.3V from iPad

## Slide 8: Schematic – Sheet 1

## Slide 9: Schematic – Sheet 2

## Slide 10: Board Layout

## Slide 11: Software Design
Microcontroller programmed in C
Utilizes libraries to interface with sensor
Communicates using serial to iPad with SLIP protocol and Zebulon MCU Message Library
iPad application is programmed in Python
  Utilizes built in serial library
  Required iPad to be rooted

## Slide 12: Results
Board works!
Able to achieve 1 Hz update rate from sensors
Low power consumption
  3.3V@30mA
  100mW
Does not severely impact battery life, not ran in background

## Slide 13: Challenges
Was unable to access serial port through Apple iOS SDK, found different method through Python
Unable to refresh GUI display continuously, receives sensor data once at startup
Gas sensors are not factory calibrated, unable to map the sensor value to a PPM
Hardware required some debugging

## Slide 14: Budget
Part | Vendor | Cost
PCB | Gold Phoenix | $50.00
Atmega328P | Mouser | $4.18
CO2 | Futurlec | $19.90
CO | Futurlec | $8.90
O3 | Futurlec | $12.90
Air Quality | Futurlec | $6.90
Barometric Pressure | Sparkfun | $24.95
iPod Connector | Sparkfun | $4.95
Humidity / Temperature | Sparkfun | $28.95
Misc | - | $20.00
Total |  | $181.63

## Slide 15: Demo
Show GUI App
Show CLI with continuous updates

## Slide 16: Future Work
Incorporate pushing data to central server for sharing with community
  Research different available frameworks with built in security and functionality
Log data with timestamp and location information (GPS not available on my iPad)
Add filters for noise on sensors
Graphing capability
Wireless connectivity to sensor board over Bluetooth
More general open source hardware to allow interface to other sensors

## Slide 17: Conclusion
Utilizing users’ mobile devices for the UI and network connectivity can make the sensor board cheaper
Opening up hardware from mobile device manufactures would make integrating these technologies simpler
General purpose hardware boards could revolutionize mobile sensing and research
Not restricted to sensor types

## Slide 18: Questions