## Slide 1: RapidSmith 2: A Framework for BEL-level CAD Exploration on Xilinx FPGAs
FPGA’2015 Feb 22-24
Travis Haroldsen
Brent Nelson
Brad Hutchings

## Slide 2: RapidSmith 1
Framework for modifying Xilinx XDL designs
Contain components and routing of Xilinx chips
Supports large number of research topics including
  Rapid design prototyping flows
  Reliability and fault-tolerant techniques
  PR frameworks
  Post-PAR debug
  FPGA security

## Slide 3: RapidSmith 1 Limitations
F:frame_buf/VGA/r_regVS<4>_rt:#LUT:D=A1
BXINV::#OFF
CYINIT:CIN
FXMUX::FXOR
_BEL_PROP::G::PK_PACKTHRU
GNDF:ProtoComp1.GNDF.1
FFY_SR_ATTR:#OFF
YUSED:#OFF
CYSELG::G
COUTUSED::0
?
RapidSmith uses string attributes to describe slice-level functionality
Little information about the types of BELs in a site
Hinders BEL-level manipulations

## Slide 4: RapidSmith 2 Improvements
Adds BEL types, properties, and interconnectivity
New BEL-level netlist
Tools to convert between XDL and BEL-level netlist
Allows modifying the packing of a design
Provides functionality for packing, placing, and routing a synthesized netlist onto Xilinx FPGAs